## Slide 2: Design and Implement a Motion Detection Based IoT System to Optimize Power Consumption Year (2023-24)
Presented By: Kartik Khandelwal Viren Sharma
Roll No.: 21UEC071 & 21UEC143
Supervisor: Dr. M.V. Deepak Nair
Assistant Professor, ECE Department
The LNMIIT Jaipur

## Slide 3: Outline:
Introduction and Literature Survey
Goals of BTP
Flow Chart
Experimental Setup
Results and Observation
Timeline and Future Goals
References

## Slide 4: Introduction and Literature Survey:
Occupancy Sensor Effectiveness: Research in smart homes demonstrates the effectiveness of occupancy sensors in optimizing energy consumption. Studies like Liu et al. (2014) showcase their ability to detect presence and adjust appliance usage accordingly [1].
Market Trend: The growth of the smart appliance market, highlighted by market research [2], indicates a consumer interest in intelligent and energy-efficient devices.
Integration Potential: Studies like Zhou et al. (2009) exploring intelligent control systems for appliances via the internet [3] further emphasize the potential for integrating IoT technology into traditional appliances.
Goals of BTP:
To design and implement a network of Radar based IoT nodes for motion detection and power optimization for classrooms and corporate board meeting rooms.
Deploy multiple detection nodes strategically within the room to achieve robust motion detection, comprehensive coverage and share power consumption to users distributed in a hierarchal way.

## Slide 5
Importance of Motion Detection in IoT:
Enhanced Security
Energy Conservation
Data-Driven Insights
Optimized User Experience
Healthcare Monitoring

## Slide 6
Flow Chart
Node Power
ON
Connecting To Network
Movement Detected ?
Turn ON Electrical Device
Wait For 10 seconds
(Adjustable Wait Time)
Connected Successfully ?
  Turn Node ON from Node-Red Dashboard
Not
Detected
Not
Connected
Detected

## Slide 7: Experimental Setup:
A Single Sensor Node Consists:
NodeMCU Module(ESP-12E)
RCWL Radar Module for detection
Electrical Relay
AC to DC Switching Mode Power Supply (SMPS)
Motion Detection Node
1
2
3
4

## Slide 8: Circuit Design:
Graphical Circuit Representation of Motion Detection Node

## Slide 9: PCB Diptrace Design:
Diptrace PCB Design
FlatCAM PCB Gerber File

## Slide 10: CNC Machine Printing:
PCB printing using CNC Machine
First PCB Printed

## Slide 11: Circuit Testing:
Short Circuit Testing:
Visual Inspection: Check for signs of shorts like solder bridges, debris, or damaged traces.
Continuity Testing: Use a multimeter to identify unintended connections between points on the PCB.
Functional Testing: Powering on the PCB and monitoring for abnormal behavior after integration of all components.
EMI/EMC Testing:
Near-field Probe: A near-field probe is used with the RSA306B Spectrum Analyzer to measure electromagnetic fields close to the PCB or its components.
Real-time DPX spectrum allows us to detect emissions not visible in a standard swept spectrum display.
EM Fields generated by relay, antenna on NodeMCU and RCWL module measured.

## Slide 12: Software Application:
Utilizing Arduino IDE for NodeMCU programming and Node-RED flows for IoT interfacing.
Node-RED Flow
Application Dashboard

## Slide 13: Observations:
Electrical relay generates harmonics of different frequencies affecting the proper functioning of the RCWL radar module.
RCWL radar module generates EM waves around 3.18 GHz.
Wi-Fi Router does not affect the functioning of RCWL.
Diagonal placement of RCWL and relay at a distance of 5.0 to 5.5cm reduces the number of false triggers significantly.
Transformer-less power supply designed earlier had high heat dissipation, requiring the integration of high-wattage resistors. Additionally, the limited output current prompted us to shift to SMPS.

## Slide 14: Results:
No Movement
Movement Detected

## Slide 15: Learning/Outcomes:
Working of Switching Mode Power Supply.
Functioning of RCWL radar module and its calibration to change the sensitivity range.
Prototyping using Zero PCB.
DipTrace designs PCBs and generates Gerber, board, and drill files, which are then converted to G-Code using FlatCAM for CNC machining.
Power measurement using DMM7510 7 ½ digital Multimeter.
Short Circuit Testing and EMI/EMC Testing using RSA306B Spectrum Analyzer.
Node Red Flow Programming and interfacing with IoT systems.
Working of MQTT protocol.

## Slide 16: Power Consumption:
Without Triggering
With Triggering
Idle Power Consumption=2.17W
Dynamic Power Consumption=3.57W

## Slide 17
15th January 2024
Literature Survey, Goal Setting
1st Prototype using Arduino
26th January 2024
RCWL Testing using 2nd Prototype
24th February 2024
SMPS Integration
9th March 2024
PCB Designing and Printing
Integration of Node RED with PCB Prototype
T I M E L I N E
20th March 2024

## Slide 18: Future Goals:
To enhance the reliability of the RCWL module and minimize false triggers by utilizing RF shielding.
To develop a power optimization algorithm and integrate power consumption analytics to optimize energy usage.
To design and implement a comprehensive database for logging lighting system data within a room.
To implement SMS notifications advising occupants to relocate for energy conservation purposes.
To include enhanced security algorithms for the complete network.

## Slide 19: References:
[1] Liu, J., Fan, Z., & Xu, X. (2014, December). Occupancy detection based on machine learning for smart homes. In 2014 IEEE International Conference on Computational Science and Engineering (CSE) (pp. 1434-1439).
[2] Grand View Research. (2024). Global Smart Lighting Market Size, Share & Trends Analysis Report By Product (LED Lighting, OLED Lighting), By Application (Indoor Lighting, Outdoor Lighting), By Region, And Segment Forecasts, 2023-2030 [Press release].
[3] Zhou, K., Li, C., Li, X., Lin, J., & Zeng, H. (2009, December). Intelligent control for home appliances via internet. In 2009 3rd International Conference on Innovative Technologies in Intelligent Systems and Industrial Applications (pp. 844-847).

## Slide 20: Design and Implement a Motion Detection Based IoT System to Optimize Power Consumption Year (2023-24)
Presented By: Kartik Khandelwal Viren Sharma
Roll No.: 21UEC071 & 21UEC143
Supervisor: Dr. M.V. Deepak Nair
Assistant Professor, ECE Department
The LNMIIT Jaipur
Thank you
and
Queries Please…

## Slide 21: RCWL Radar Module’s Working and Features
RCWL Module: Microwave radar motion sensor module
Operates on Doppler effect principle.
Emits signals around 3.18 GHz frequency omnidirectionally.
Circuit comprises of a microwave transceiver, mixer and a lower frequency section with RCWL-9196 IC.
Observed Working Range: 4-5 meters.

## Slide 22: NodeMCU Module:
Open-source firmware and development kit for IoT prototyping.
ESP-12E: Low-cost Wi-Fi microchip with TCP/IP stack and microcontroller capability.
GPIO Pins: NodeMCU offers 17 GPIO pins (11 usable) and PWM support (at a time on 6 pins).
Communication Interfaces: Supports UART, SDIO, SPI, I2C and IR remote control.
Wi-Fi Connectivity: Operates at 2.4 GHz with WPA/WPA2 support for secure connections.
NodeMCU Pinout

## Slide 23: Electrical Relay and AC-DC SMPS
SPDT relays switch between two circuits with one common terminal and two others (Normally Open and Normally Closed).
When energized, the common terminal connects to Normally Open; when not, it connects to Normally Closed.
SMPS efficiently convert AC to DC through rapid voltage switching.
SMPS provide stable voltage output for consistent power.
Smaller size of transformer coils.

## Slide 24
Feature | RCWL-0516 Microwave Radar Sensor | PIR Sensor | Ultrasonic Sensor
Detection Method | Microwave Radar(3.18GHz) (Doppler Effect) | Passive Infrared (PIR) | Ultrasonic Waves (30–500 kHz)
Detection Range | 5-7 m | 10-12 m | 2-4 m
Detection Area | Omnidirectional | Limited | Limited
Environmental affect | Less affected by temperature and humidity | Sensitive to temperature and humidity | Affected by temperature and humidity
Advantages of RCWL-0516 - |  | High sensitivity and accuracy Less affected by environmental factors Low susceptibility to false alarms Omnidirectional detection | 
Motion Detection Sensor Modules Comparison Table

## Slide 25
Feature | NodeMCU (ESP8266) | ESP32
CPU | Tensilica Xtensa LX106 | Dual-core Tensilica Xtensa LX6
CPU Frequency | Up to 160 MHz (SW limited to 80MHz) | Up to 240 MHz (single-core) Up to 160 MHz (dual-core)
Wi-Fi Connectivity | Built-in | Built-in
ADC | 10-bit | 12-bit
GPIO | 17 GPIO Pins | 34 GPIO Pins
Approx. Cost | ₹160-170 | ₹390-400
Why NodeMCU?

## Slide 26
RCWL-0516 EMI/EMC Testing using RSA306B Spectrum Analyzer

## Slide 27
Arduino Code Snippet

## Slide 28
Serial Monitor Status

## Slide 29
1st Prototype-15/01/24

## Slide 30
2nd Prototype-26/01/24

## Slide 31
MQTT Protocol

## Slide 32
Transformerless Power Supply